## Slide 1
Rugged Monitoring designs, manufactures and commercializes rugged fiber optic temperature sensors and monitors for laboratories, utilities, industrial, process, medical and OEM applications.

## Slide 2
Rugged Monitoring
Vision
Leading provider in fiber optic based sensing solutions dedicated to offering the best in class reliability & service.
Be first in mind and choice for customers by delivering leading edge, innovative and reliable monitoring solutions
Reliable, high performance, precision, rugged customizable sensors and monitoring solutions
Commitment
Mission

## Slide 3
Our Plan
Be a leading fiber optics based sensing solution provider to Utilities , E- Mobility and Medical industry verticals
E-Mobility
Medical
Energy/ Utilities

## Slide 4
Industries We Serve
E-Mobility
Medical
RF / Microwave
Industrial
Research Lab
Utilities

## Slide 5
Our Plan
E-Mobility
Medical
Utilities
Near Term
Mid term
GaAs Temperature
Fluorescence Temperature
Pressure
Vibration
Partial Discharge
Light
GaAs Temperature
Fluorescence Temperature
FBG Temperature
Pressure
Vibration
Fabry-Pérot Pressure
Fluorescence Temperature
GaAs Temperature
Sensing Solutions:
Initial Focus

## Slide 6
E-Mobility Plan
Battery Simulation
Battery Test Stands
Motor Testing
Power Train Testing
Power Electronics
Li-ion Battery packs
Power Cables
Fast Chargers
Sensing Solutions for:
Leading Temperature, Pressure, Vibration, Partial discharge sensing solutions for E-Mobility segments that are undergoing major design transformations with EV’s.

## Slide 7
Medical Plan
Equipment
Neo natal
Sensing Solutions for:
Leading Temperature, Pressure, Vibration sensing solutions for Medical segments that are undergoing next generation transitions.
Clinical Trials
Power Electronics
Interventional
Bio Medical

## Slide 8
Presentation Outline, with Focus on Transformer Applications
Rugged Monitoring Products
Importance of Transformer Hotspot Monitoring
Traditional Measurement Methods
Fiber Optic Temperature Measurement Advantages
Fiber Optic Measurement Equipment
Recommendations on Probe Installation

## Slide 9
Presentation Outline
Rugged Monitoring Products and Applications
Importance of Transformer Hotspot Monitoring
Traditional Measurement Methods
Fiber Optic Temperature Measurement Advantages
Fiber Optic Measurement Equipment
Recommendations on Probe Installation

## Slide 10
Products
Fiber Optic Sensors
Monitors
Accessories & Software

## Slide 11
Products Range
L201
T301
R501
R&D Applications
2-8 Channels
Continuous Monitoring
4-24 Channels
Rack Mount
8-256 Channels

## Slide 12
Sensors Range
Lsens C
Lsens B
Lsens P
Lsens R
Lsens T
Tsens
Cryogenic
As low as 4°K
Medical
0.3 mm Dia
Electric Vehicle
0.7 mm Dia
Industrial
1.7 mm Dia
Chemical
1.1 mm Dia
Hot Spot, Transformers
3 mm Dia

## Slide 13
Radio Frequency
Chemicals
High voltage
Radiation
Microwave
Immunity to Environments
13

## Slide 14
Water Proof Sensors
Advantages
Point Measurement
No Calibration
Rugged Sensors
48 hours Service Response
Designed for Temperature
Unbeatable Price / Value

## Slide 15
Electric Vehicle & Battery Testing
Applications
Microwave Chemistry
OEM integration with MW manufacturers
Transformer Hot Spot Monitoring
Sterilization, Pasteurization Process
MW oven design and testing

## Slide 16
Medical Equipment Manufacturers
Applications
Cryogenics
Process Industries
PCB Development & Testing
Food & Beverage
R&D Labs

## Slide 17
Presentation Outline
Rugged Monitoring Products and Applications
Importance of Transformer Hotspot Monitoring
Traditional Measurement Methods
Fiber Optic Temperature Measurement Advantages
Fiber Optic Measurement Equipment
Recommendations on Probe Installation

## Slide 18
Transformer Hot Spot Monitoring System Diagram
Tsens Transformer Sensor
Feedthroughs
Tank Wall Plate
Fiber Optic Extension Cable
T301 Monitor

## Slide 19
Importance of Hot Spot Monitoring
To assess the insulation aging rate and resulting remaining life
  Rationale: Winding temperatures have a direct impact on insulation aging
To maximize the load potential safely
  Rationale: Winding temperatures limit the load potential
To better manage assets and drive revenue generation strategies
Normal Kraft paper
Thermally Upgraded Paper

## Slide 20
Presentation Outline
Rugged Monitoring Products and Applications
Importance of Hotspot Monitoring
Traditional Measurement Methods
Fiber Optic Temperature Measurement Advantages
Fiber Optic Measurement Equipment
Recommendations on Probe Installation

## Slide 21
Traditional Measurements – WTI

## Slide 22
Limitations of Traditional Measurements, with WTI’s
Regardless of the sophistication level of Modern WTI’s (some have microprocessors to calculate), they still simulate or approximate the real temperatures present in the windings
The time response of WTI’s is based on oil time constant, not winding’
WTI’s are rarely calibrated correctly
  Theory says that they can be calibrated only if fiber optic sensors are used to validate them
Display errors of 5 to 10 degrees C, or more, are common

## Slide 23
Traditional Measurements – Heat Run Tests
“Heat Run” tests reveal average winding temperature under rated load
What is of interest for insulation aging is the winding hottest spot temperature (temperature is not uniform around the winding)
Temperature is highest at top of winding
  Oil is hotter
  Stray losses in winding are higher
  Winding insulation often calls for more paper to provide better insulation against voltage surges
Bottom of winding
Top of winding
Radial Eddy Loss
Axial Eddy Loss
DC losses (Loss = RI2)
Core



## Slide 24
Traditional Measurements – Model
Top-Oil Temp.
Hot-Spot Temp.
Average Winding Temp.
Hot-Spot Rise
Temperature (
o
C)
Winding
Oil
Top Oil Temp.
Hot Spot Temp.

## Slide 25
Winding Hotspot Temp Model
Winding hot-spot temp.
=
Top-Oil Temp.
+
Hot-spot rise at rated load
* (%Load)2m
For any load level, the hottest winding temperature is assumed to be:
For several decades, this method was a standard feature:
  IEEE C57.91 - 1995 “IEEE Guide for Loading Mineral Oil Immersed Transformers”
  IEC 60354 - 1991 “Loading Guide for Oil-Immersed Power Transformers”
This simplified method is now regarded as inadequate to estimate the aging of transformers given increasing occurrences of overloads
  IEEE and IEC are proposing new methods to take account of (neglected in the previous equation):
  True oil temperature in the cooling duct
  Change in winding resistance with temperature
  Change in oil viscosity with temperature
  The effect of tap changers
  Oil inertia in case of sudden overload of large magnitude

## Slide 26
Presentation Outline
Rugged Monitoring Products and Applications
Importance of Hotspot Monitoring
Traditional Measurement Methods
Fiber Optic Temperature Measurement Advantages
Fiber Optic Measurement Equipment
Recommendations on Probe Installation

## Slide 27
Winding Hot Spot Temperature Model
The evolution in calculation methods indicates:
  Methods used until now are not very accurate
  New methods will require additional parameters that are not always readily available
  New models still rely on information provided by the transformer manufacturer and not always validated
  Accurate hot spot temperature knowledge allows for better estimation of transformer MVA performance.
Direct Measurement of Winding Temperature with Fiber Optic Sensors is Recognized as the Best. method

## Slide 28
Presentation Outline
Rugged Monitoring Products and Applications
Importance of Hotspot Monitoring
Traditional Measurement Methods
Fiber Optic Temperature Measurement Advantages
Fiber Optic Measurement Equipment
Recommendations on Probe Installation

## Slide 29
Monitor & Accessories
Extension Cable
Tank Wall Plate
Feedthrough
Tsens Probe
Interface Box
T301 Monitor

## Slide 30
T301 Monitor
Specifications
Accuracy of ±1 °C, resolution of 0.1 °C
“Optical System Integrity Check” feature
Rugged and sturdy cast aluminum construction
One monitor supports up to 24 optical temperature sensors
8 channel fully programmable analog outputs, V or mA
8 programmable Form-C relays (5A)
Dedicated system fault relay
Based on market leading GaAs technology for long term reliability
Light sources have an estimated life of 300 years
Environmental temperature range: -40 to +72 oC
8 GB memory industrial grade removable microSD card (option)
  Enough for at least 10 years of data, @10sec rate
Built in Webserver, with 1 Gigabit Optical Ethernet (option)
Standard USB and serial RS-485 interfaces (with Modbus, DNP3 and IEC 60870-5-101)
24 or 48 VDC, ~ 20 watts
Full set of advance communication protocols
  IEC 61850, Modbus over Ethernet, DNP3 and IEC 60870-5-104
Optional fiber SFP transceiver, an industry standard
  Benefit: Redundant Ethernet communication
A Rugged Monitoring first:
An internal reference optical sensor
insures optical module integrity

## Slide 31
Monitor / Software – Features
T301 Monitor
4 - 24 Channels
Onboard Data logging, on microSD
Industrial grade Electronics
Gigabit Optical Ethernet option
Analog output option (8 outputs)
Industry standard protocols
Designed for harsh environments
0.1 °C Resolution
Built in Webserver (with Ethernet)
Built in Optical Integrity Check
Rugged Connect Software
Single Suite for all devices
Designed for Periodic and Continuous Monitoring
Easy to use Analytics
Export Data for Analysis
LabVIEW / MATLAB / Python Drivers
Proprietary Algorithms
Customizable for System integration
Can generate configurations for virtual instruments

## Slide 32
T301 Monitor Software – User First – Ease of Use
Webserver /Ethernet
Rugged Connect
Supports up to 4 instruments
  Each with its own USB interface
Supports all popular serial protocols
  Modbus, DNP 3 and IEC 60870-5-101
Data logging and graphing
Supports virtual instruments (re projects)
Similar “Look & Feel” as Rugged Connect
Supports all popular Ethernet protocols
  Modbus, DNP 3, IEC 60870-5-104 & IEC 61850

## Slide 33
Transformer Sensors (Tsens)
Specifications
Features
Improved design (patent pending)
Measuring range: -80 °C to 250 °C
Response time of ~1 sec
Available in any lengths, up to 25 m (or more)
With industry standard ST connector, with zirconia ferrule
Solid Torlon disc tip, diameter 9 mm (patent pending)
Suitable for dry-type and oil-filled transformers
Compatible with all types of transformer oil, including ester type
Meets and surpasses ASTM D3426 and D-149 standards
Extremely low PD performance (< 2pC)
Very high resistance to pulling (> 60 N)
Compatible with kerosene vapor drying process
With or without disc tip
  Disc version recommended for all applications
Patent Pending

## Slide 34
Feedthrough
Features
Specifications
With zirconia connectors for better optical light transmission
Stainless steel 316L construction
Standard ¼” NPT
  Other sizes also available
Wide temperature and pressure ranges
Easy installation
No O-rings design
Tested to 10,000 psi

## Slide 35
Extension Cable
Features
Specifications
With zirconia connectors (ferrules)
3 mm OD
Maximum temperature: +85 °C
Available in any lengths, up to 99 meters
PVC sheathing with Kevlar reinforcement
Dielectric Torlon connectors available

## Slide 36
Dielectric Connector
Features
Specifications
With zirconia connectors for better optical light transmission
Torlon construction
Entirely dielectric design
Repair kit is available
Best to repair damaged probes in the field
Can also be used to extend already installed probes that are found to be too short

## Slide 37
Extension Bundle
Specifications
17 mm OD
For up to 24 fibers
Fanouts of 50 cm at each end
Steel reinforced
Maximum temperature: +100 °C
Available in any lengths, up to 25 meters, or more

## Slide 38
Tank Wall Plate & Interface Box
Tank Wall Plate
Interface Box
Features
Specifications
With O-Ring or gasket
  Gasket is customer supplied
Compatible with Interface I-Box
  Optional bolting provision
Diameter of 275 mm
Stainless steel 316L construction
For up to 25 feedthroughs
Features
Specifications
Leak proof design
Meet IP66 rating
Size 200 x 200 mm, 150 mm high
With neoprene gasket
Stainless steel 316L construction throughout

## Slide 39
Intrinsically safe
Immunity to Magnetic and RF Fields
Customizable to every need
Harsh environments
Highly Corrosive applications
Fiber Optic Temperature Sensors
RUGGED MONITORING

## Slide 40
Presentation Outline
Rugged Monitoring Products and Applications
Importance of Hotspot Monitoring
Traditional Measurement Methods
Fiber Optic Temperature Measurement Advantages
Fiber Optic Measurement Equipment
Recommendations on Probe Installation

## Slide 41
Recommendations on Probe Installation – 1
Details of probe construction

## Slide 42
Recommendations on Probe Installation – 2
Recommendations:
Probe with disc option (9 mm) is recommended for ALL applications
Always mount probes in pressboard material, 3 mm thick or more
Unless you want to measure oil temperature, make sure sensor is not in direct contact with circulating oil
Try to minimize the number of bends, with minimum bending radius of 5 cm or more
If you need to coil extra length of probe cable, make sure coil diameter is at least 30 cm.

## Slide 43
Recommendations on Feedthrough Installation
Recommendations:
Thread sealant is recommended
  Loctite 567 or 3M Rite-Lok PS67 or PS92
  Apply a small quantity on the feedthrough tread before screwing it to the tank wall plate
Torque by “feeling” and by number of turns
  With NPT threads, it is not possible to specify a recommended torque value, so we need to go by “feeling” (just like all plumbers are doing)
  The recommendation is to hand tight the feedthrough and then add ~2 turns with a wrench fitted with a 14 mm socket
You will need to apply substantial torque, especially if you are not using any sealant. A 30+ cm wrench is recommended, as shown
Before Tightening
After Tightening

## Slide 44
And finally, A Big Focus On Product Quality
We use zirconia ferrules throughout
  This gives connector concentricity of ~ 5 µ vs. ~ 20 to 30 µ with metal ferrules
    A strong optical signal is always best
  This also results in much improved corrosion and scratch resistance
Probes exhibit the strongest pulling forces in the industry
Probes exhibit the lowest PD (partial discharge, less than 2 pJ) in the industry
An Optical Integrity Check is automatically performed at power on (T301)
We use nickel plated brass connectors in our feedthroughs
  This results in much improved corrosion resistance
A new Interface Box, in stainless steel throughout, guaranteed to be leak proof
  Meets IP66 ratings

## Slide 45
Suggested Configurations

## Slide 46
Leading Fiber Optics Experts
Best in class response and service
Rugged Designs
Patented Technologies
Commitment to Innovation and quality
Why RUGGED MONITORING?
46
Thank you !
Questions ?